## Slide 1: How to standardize Aspergillus PCR protocols for testing various specimens
Dr P. Lewis White
FRCPath, FECMM
Public Health Wales, Microbiology Cardiff

## Slide 2: Disclosures
Company | Advisory Panel | Sponsorship | Grant | Speaker
Gilead | ✓ | ✓ | ✓ | ✓
MSD |  |  |  | ✓
Bruker |  | ✓ | ✓ | ✓
Launch |  | ✓ |  | ✓

## Slide 3: Know your process
Disease manifestation
Specimens available
Underlying condition
Frequency of testing
Testing strategy
Incidence
Organ infected
Targets available
Governs methods
Result interpretation
Underlying condition
Frequency of testing
Testing strategy
Disease manifestation
Contamination
Inhibition

## Slide 4
IA Pathology
Specimens available
Literature review/Expert discussion
Determine preferred specimens/targets
Achieving standardisation – Step 1
Testing strategy
Incidence
Notes: 4

## Slide 5: Know your disease

## Slide 6: Invasive Aspergillosis – Disease process
DOH!

## Slide 7: Aspergillosis – Disease spectrum
Cutaneous
Sinusitis
Cerebral
Pulmonary
Endocarditis
Osteomyelitis
Disease presentation,
Invasive, non-invasive, localised, allergic, chronic, acute:
Optimal Specimen type
Common species:
A. fumigatus, A. flavus, A. niger A. terreus, A. nidulans, A. versicolor
Disseminated
Analytical specificity

## Slide 8: Determining Analytical Specificity
Morton et al. Medical Mycology 2016
Range of Aspergillus sp detected
Cross reactivity
18 DNA samples
    12 from Aspergillus sp
    6 from other fungi
28 centres/33 datasets

## Slide 9: Analytical Specificity - Summary
Current Aspergillus PCR assays are better suited for detecting A. fumigatus
Inferior detection of other Aspergillus species.
  Geographical variation is important when developing assays
Genus sp assays increase detection range but compromise analytical specificity
Current strategies for IA are better suited to excluding disease – assay sensitivity is paramount
The use of an Aspergillus genus specific PCR assay targeting the rRNA genes is preferential.
Morton et al. Medical Mycology 2016

## Slide 10: Sample Choices

## Slide 11: IA and the host
White and Barnes 2018

## Slide 12: Choice of Specimen for IA
  BAL
    Inhalation of Aspergillus spores
    Invasive
    Extensive successful studies
  CSF/Tissue samples
    Limited studies
    Invasive
  Serum/Plasma
    Extensive successful studies
    Targets Circulating DNA
  Whole Blood
    Extensive successful studies
    Targets DNA, fungal fragments
    Extended extraction procedure
Screening/Pre-emptive
Diagnostic Confirmation
Notes: The choice of specimen can limit the available target type and may have effects on the PPV of the assay. Several publications have linked PCR positive BAL specimens with cases of IA. However inhalation of spores and/or colonisation of the lung may give rise to false positive results. In addition, the invasive nature of obtaining a BAL specimen often limits the use of the procedure. This is also true for CSF sample and the difficulty in obtaining control samples, initial, and repeat clinical specimens has lead to limited studies. Nevertheless PCR positive CSF samples should be considered significant.

## Slide 13: Biomarker Performance – BAL
Infrequent test
Diagnostic: Confirms disease in symptomatic patients
  High Specificity / PPV
Parameter | GM-EIA |  | PCR |  | 
Reference | Zuoa | Guob | Tuonc | Sund | Avnie
Sample | BAL | BAL | BAL | BAL | BAL
Sensitivity | 83.6% | 85.7% | 78.4% | 79.6% | 76.8%
Specificity | 89.4% | 89.0% | 93.7% | 94.1% | 94.5%
aZuo et al. PLoS One. 2012;7(8):e43347; bGuo et al. Chest 2010; 138:817-824; cTuon FF. Rev Iberoam Micol. 2007;24:89–94; dSun et al. Plos One 2011; 6(12): e28467; eAvni et al. J Clin Microbiol. 2012;50:3652–8; fMutschlechner W, et al. Transplantation. 2015;99:e140–4
LR +tive: >12
Overall comparable performance
Despite limited standardisation
GM-EIA: galactomannan enzyme immunoassay; PPV: positive predictive values
BDG – Poor specificity (38.5%)f
Culture – Poor sensitivity (50% IA cases)

## Slide 14: Biomarker Performance- Blood
High frequency screening test
Excludes fungal disease
  High sensitivity / NPV
Beneficial for low incidence disease
aLeeflang et al. J Clin Epidemiol. 2009;62:5-122009; bPfeiffer et al. Clin Infect Dis 2006; 42:1417-27; cLamoth et al. Clin Infect Dis. 2012;54:633–43; dKarageorgopoulos et al. Clin Infect Dis. 2011;52:750–70.; eHe et al. J Microbiol Immunol Infect 2015;48:351–61; fMengoli C, et al. Lancet Infect Dis. 2009;9:89–96; gArvanitis M, et al. J Clin Microbiol. 2014;52:3731–42
Parameter | GM-EIA |  | β-D-Glucan |  |  | PCR | 
Reference | Leeflanga | Pfeifferb | Lamothc | Karageorgopoulosd | Hee | Mengolif | Arvanitisg
Sample | Serum | Serum | Plasma/Serum | Plasma/Serum | Plasma/Serum | Blood | Blood
Sensitivity | 79.3% | 79.3% | 56.8% | 77.1% | 77.0% | 88.0% | 84.0%
Specificity | 80.5% | 86.3% | 97.0% | 85.3% | 81.3% | 75.0% | 76.0%
LR -tive: 0.15 = Negative results exclude IAf
Comparable performance despite limited standardisation
IA: invasive aspergillosis; LR: likelihood ratio; NPV: negative predictive values; PCR: polymerase chain reaction

## Slide 15: Determine preferred specimen
Based on optimal use of test
  IA Incidence: 5-15%
  Screening strategy
Overuse of unnecessary AFT
Ease of obtaining samples
  Invasive vs Non Invasive
  High frequency
Blood
  WB or serum or plasma
BAL methodology: secondary evaluation
  Confirmation of IA

## Slide 16: Potential targets in blood
Invading hyphal fragments
Circulating DNA
Release Mechanism:
Hyphal damage
Interstitial pressures
Autolysis, immune system, antifungal activity
DNAemia
Viable
Angioinvasion and dissemination
Non viable
Platelet attachment Phagocytosis Alveolar MC translocation

## Slide 17
Determine preferred specimens/targets
Determine optimal protocol through analytical validity
Distribution of QC panels – contrived samples
Evaluate existing methodology
Analysis of results
KEY PARAMETER
Multi-centre evaluation of recommendations
Provide methodological recommendations
Achieving standardisation – Step 2
Acceptable analytical performance
Methodological Recommendations confirmed
Distribution of QC panels – contrived samples
Analysis of results
KEY PARAMETER
Notes: 17

## Slide 18: Extraction recommendations
 | Serum/Plasma Testing | Whole Blood testing
Sample type | N/A | EDTA only
Sample volume | ≥0.5ml | ≥3.0ml
Potential target | Free circulating DNA | Phagocytosed fungal fragments
Extraction requirements | Commercial extraction kits | Red and White cell lysis, Bead-beating, commercial extraction kits.
Elution volume | Elute in <100µl, | 
Special requirements | Screen all reagents for contamination with fungal DNA. Positive and negative extraction controls recommended. PCR testing in duplicate. Perform an IC PCR (Ct typical of Aspergillus PCR +tve, not human DNA, can be incorporated into extraction process) | 
“Nucleic Acid extraction is the critical step”
White et al 2010a, 2010b, 2011 and Loeffler et al. 2015

## Slide 19: Achieving standardisation – Step 3
Methodological Recommendations confirmed
Animal model validation
Multi-centre clinical evaluation
Define clinical validity and utility
Inclusion in disease defining criteria

## Slide 20: Dynamics of release
IAAM - Guinea pig inhalation IA model
  43 immunosuppressed (cyclophosphamide and cortisone acetate)
    30 exposed to A. fumigatus – Cases
    13 immuosuppressed high risk controls
  13 Immunocompetent low risk controls
  Euthanized: 1 hour, 5, 7 and 9 days
Testing
  Aspergillus PCR
    3ml EDTA WB for testing by 3 EAPCRI centres
    0.5ml serum for testing by 1 EAPCRI centre
  GM-EIA and β-D-Glucan
    Performed on serum by IAAM centre
White et al. JCM 2016

## Slide 21
Assay positivity across the experiment
White et al. JCM 2016
Cases
Controls
1) PCR positivity is an early indicator of exposure/infection:
pre-emptive strategies
Primary test in screening
Notes: Galactomannan, β-d-glucan, and PCR positivity for the individual time points across the time course of the experiment: (a) infected animals and (b) uninfected animals. Galactomannan positivity was determined using a threshold index of 0.5, and β-d-glucan positivity was determined using a threshold of 80 pg/ml. All PCR positives were confirmed by repeat testing.

## Slide 22: Monitoring disease progression
White et al. JCM 2016
GM/BDG are indicators of disease progression

## Slide 23
Assays | Sensitivity (%) | Specificity (%) | Accuracy (%) | LR+ | LR- | AUC
WB PCR | 73 | 92 | 82.7 | 9.5 | 0.3 | -
Serum PCR | 65 | 79 | 72.0 | 3.1 | 0.4 | -
GM | 68 | 80 | 74.5 | 3.4 | 0.4 | 0.77
BDG | 46 | 100 | 74.5 | >455 | 0.6 | 0.82
Serum/WB PCR | 91/33 | 65/100 | 77/68 | 2.6/>330 | 0.1/0.7 | 0.84
BDG/WB PCR | 86/24 | 91/100 | 89/64 | 9.6/>240 | 0.2/0.8 | 0.90
GM/WB PCR | 100/33 | 78/96 | 89/66 | 4.5/8.3 | <0.001/0.7 | 0.91
BDG/Serum PCR | 76/33 | 74/100 | 75/68 | 2.9/>330 | 0.3/0.7 | 0.79
GM/Serum PCR | 90/43 | 61/96 | 75/70 | 2.3/10.8 | 0.2/0.6 | 0.82
GM/BDG | 81/38 | 83/100 | 82/70 | 4.8/>380 | 0.2/0.6 | 0.85
White et al. JCM 2016

## Slide 24
Assays | Sensitivity (%) | Specificity (%) | Accuracy (%) | LR+ | LR- | AUC
WB PCR/GM/BDG | 100/67/14 | 78/96/100 | 89/82/59 | 4.5/16.8/>140 | <0.001/0.3/0.9 | 0.95
Serum PCR/GM/BDG | 100/48/33 | 61/96/100 | 80/73/68 | 2.6/12/>330 | <0.002/0.5/0.7 | 0.88
WB/Serum PCR/BDG | 90/71/10 | 65/100/100 | 77/86/57 | 2.6/>710/>100 | 0.2/0.3/0.9 | 0.90
WB/Serum PCR/GM | 100/81/14 | 57/91/100 | 77/86/59 | 2.3/9/>140 | <0.002/0.2/0.9 | 0.92
All four assays | 100/91/44/10 | 57/91/100/100 | 77/91/73/57 | 2.3/10.4/>429/>950 | <0.001/0.1/0.6/0.9 | 0.95
Overall PCR performance is comparable with established antigen tests
Combination testing is optimal: PCR, β-D-Glucan and GM
White et al. JCM 2016

## Slide 25: Standardization has improved Clinical Performance
EAPCRI recommendations improved PCR performance
  Independent analysis
Sensitivity: 87% vs 82%
Specificity: 98% vs 85%
Not total compliance with EAPCRI recommendations (1 deviation)
Arvanitis M, et al. J Clin Microbiol. 2014;52:3731–42

## Slide 26: EORTC/MSG definitions - Proposal
Aspergillus PCR– Mycological criterion
  Serum, Plasma, WB
  BAL
  2 or more consecutive positives
  Positive in both blood and BAL
  Combination biomarker testing
    PCR and GM >0.5
      Blood or BAL
    PCR and BDG >80pg/ml
      Blood or BAL?
Manuscript in preparation

## Slide 27: What about BAL
Manuscript in preparation
Tomorrow @ 10.30: S10.2 ISHAM Working Group: Fungal PCR Initiative Room E106

## Slide 28: Summary
Know your disease
  Incidence
  Pathology
Know your preferred sample type
  Testing strategy
  Obtainability
Know your potential NA sources
  Between samples
  Suitability of extraction process
NA extraction is critical
  Evaluate and optimize
  PCR amplification is only as efficient as the NA extraction technique will allow.
PCR – Determine analytical specificity
International standard for Aspergillus PCR
Extensive collaboration essential
  No room for egos!
“You never really learn much from hearing yourself speak.”

## Slide 29: Acknowledgements
All members of the EAPCRI, now known as the FPCRI
IAAM/AsTeC
Public Health Wales

## Slide 30
Negative validation
IA Pathology
Specimens available
Literature review/Expert discussion
Determine preferred specimens/targets
Determine optimal protocol by analytical validity
Distribution of QC panels
Evaluate existing methodology
Analysis of results
KEY PARAMETER
Multi-centre evaluation of recommendations by QC
Provide methodological recommendations
Animal model validation
Positive validation
Negative validation
Multi-centre clinical evaluation
Define clinical validity and utility
Inclusion in disease defining criteria
Protocol reassessment
Multicentre QC evaluation of modified protocol
Positive validation
Negative validation
Achieving standardisation
Testing strategy
Incidence
Notes: 30